UART power control-3

Problem
The Serial.end() does nothing and hence the UART stays active. This impacts unexpected wake-up from deepsleep and extra power consumption during sleep.

Unlike SPI or WIRE, the UART is linked (HardwareSerial.c) with MBED at the moment of creating the constructor. With SPI and WIRE this is happening during begin().

I have already created and documented a solution with keeping the current structure in HardwareSerial.c, but wanted to test an approach as with SPI and Wire.
That was the second solution with many changes in HardwareSerial.

This third soltution is based on the learnings of the two earlier solutions. Much easier and cleaner.

Description
There is an empty function Serial_free() in Serial_api.c, part of Apollo3 target. It can be called from mbed (SerialBase.c) function _deinit(). This function is set as private and _deinit() can not be called without changes.
Changes are needed in :
- HardwareSerial.c
- HardwareSerial.h
- UnbufferedSerial.h
- Serial_api.c

Changes to HardwareSerial.h (1 change)

Add a variable in protected area of the class :

bool _DoReInit = false;

Changes to HardwareSerial.c (2 changes)

1. Add a check in the top of UART:begin() whether reinitialize is needed as UART::end() has been called before

     if (_DoReInit) {
        UnbufferedSerial::_init();
        _DoReInit = false;
    }

2. Add in UART::end() :

void UART::end( void ){

    // close down UART
    UnbufferedSerial::_deinit();
    _DoReInit = true;
}

In mbed-os/drivers/UnbufferedSerial.h (1 change)

Around line 158 add

using SerialBase::_deinit;
using SerialBase::_init;

To the list :
    using SerialBase::readable;
    using SerialBase::writeable;
    using SerialBase::format;
    using SerialBase::attach;
    using SerialBase::baud;
    using SerialBase::RxIrq;
    using SerialBase::TxIrq;
    using SerialBase::IrqCnt;

In TARGET_APOLLO3/device/serial_api.c (1 change)

Serial_free() call is now getting content.

void serial_free(serial_t *obj) {

    MBED_ASSERT(obj->serial.uart_control->handle != NULL);

    //
    // check for initialized
    //
    if (! obj->serial.uart_control->handle){
        return;
    }

    //
    // Wait for all of the traffic in the TX pipeline to be sent.
    //
    am_hal_uart_tx_flush(obj->serial.uart_control->handle);

    //
   // Power down the UART
   //
    MBED_ASSERT(AM_HAL_STATUS_SUCCESS == am_hal_uart_power_control(obj->serial.uart_control->handle, AM_HAL_SYSCTRL_DEEPSLEEP, false));

    //
    // de-initialize handle
    //
    MBED_ASSERT(AM_HAL_STATUS_SUCCESS == am_hal_uart_deinitialize(obj->serial.uart_control->handle));

    //
    // reset handle (to enable re_init next time)
    //
    obj->serial.uart_control->handle = 0;
}